## Slide 2
Payload integration company
  Safety and Integration Requirements
  Manifesting
  Operations Planning Products and Procedures
  Functional Testing
  Payload delivery to NASA for launch
  On-Orbit Operations
  Return of the payload to Earth
NanoRacks’ Role

## Slide 4: Safety Inputs (L-5.5 Months) Operational Inputs (L-5.5 to 3.5 Months)
Safety and Manifesting Inputs
  All information as documented in the safety data template needs to be provided
  All design aspects need to be covered. This includes, but is not limited to: bill of materials (and how much of it), parts list, and how exactly these all fit together (the types of fasteners or glue, etc.)
  Provide electrical diagrams and labeled CAD drawings and anything else to help us understand your payload
  Safety schedule based on an April launch:
    Initial documentation submittal to NanoRacks
    NanoRacks submittal to NASA
    Phase I/II Safety Review with NASA
    Second documentation submittal to NanoRacks
    NanoRacks Submittal to NASA
    Phase III Safety Review with NASA
Operation inputs
  Installation and cold stow requirements
  Timelines for planning (use an exact date and ranges)
  Payload handling requirements
The earlier you provide safety and operational inputs, the better we can guide you through the NASA safety process.
  Late inputs and any changes to hardware after Phase III information is submitted will impact the schedule – possible missed flight

## Slide 5: Safety Inputs (L-5.5 Months) Operational Inputs (L-5.5 to 3.5 Months)
  Main areas of concern for Safety
    Batteries/capacitors
    Materials/toxicity/biologicals
      Chemicals/liquids/gasses/powders/greases
      Biologicals – must be purchased from a qualified supplier
        No contamination, pesticides, it is what it is – Vendor CoC
      Nonmetallics/glues/adhesives/sealants/greases/plastics
      Metallics
      Compatibility (may have to perform compatibility test)
      Levels of containment
        Verify each level independently
    Configuration/design (CAD/Solidworks, drawings, schematics)
    EMI
      Cable vs. no Cable
      Inside rack vs. outside rack
      Plastic case vs. aluminum case
    Rotating Equipment (fans, motors)
    Magnets
    Fasteners – secondary locking features
    Shatterable materials
    Workmanship – staking, wire restraint, sharp edges
    Electrical
      High voltage sources
      Maximum voltage/current
      Wire size, circuit protection
      Batteries/capacitors
        Acceptance and qualification testing may be required
      Grounding/bonding
    Crew operations/crew time

## Slide 6
Fit
  Dimensional properties
  Physical connection between the NanoRacks Platforms and your payload
Form
  Inspecting payloads to verify design for safety purposes
  Inspecting for structural integrity
Function
  Software interface between the NanoRacks Platform and your payload
  Ground testing to ensure proper functionality on-orbit
Functionality Testing (No later than 3.5 months)

## Slide 7
Since NanoRacks will be thoroughly inspecting your NanoLab (inside and out, as well as code), please provide instructions on how to disassembly your payload, your code, and special handling requirements
Your science should NOT be loaded into the NanoLab at this time (this is only a hardware and software test).
Functionality Testing (No later than 3.5 months)

## Slide 8: Handover from NanoRacks to NASA
Handover from you to NanoRacks will take place anywhere from L-45 days to no later than L-32 hours.
HFIT
  Astronaut handling
Handover timeline
  Launches rarely go as planned
  48-hour scrub scenario with a 2 hours refresh period.
  While your payload may be handed over a few hours from launch, there is a high probability your payload will not be installed until days later (most payloads are not installed until at least 5 days after handover to NASA).

## Slide 11
USB Ports
  USB ports need to be recessed to be flush with the outer surface of the module
  Solder a 3 inch small gauge wire to the outside casing of the USB port. This wire will be used by NanoRacks to ground the payload before handover to NASA. Soldered wires are expected to pass a tug test.
Exterior of the NanoLab
  For crew safety concerns, nothing should be sticking out of exterior housing of the NanoLab.
NanoLabs Lessons Learned

## Slide 12
Accessibility
  The NanoLab is small, which can make it difficult space to work in. Keep accessibility in mind when designing your payload so that it will be easier to work with throughout the manufacturing and testing process.
  Screws instead of glue
Environmental Awareness
  Your payload will be sharing the space with other payloads and astronauts. Design your payload so that there is a minimal impact on its surrounding environment.
NanoLabs Lessons Learned

## Slide 13
Fasteners
  Size 4-40 countersunk screws for the exterior of your NanoLab
  Size 4-40 button head or pan head screws for the interior of your NanoLab
  Consider using allen wrenches instead of cross-tip screwdrivers
Communication
  NanoRacks, CASIS, Texas A&M, and your mentors are here to help. If you have any questions, please don’t be afraid to ask us. The earlier we know of the situation, the sooner we can come up with a solution that fits all safety, integration, operational, and payload customer needs requirements.
NanoLabs Lessons Learned

## Slide 14
For a more through guide to payload requirements concerning NanoLabs, you can refer to the NanoLabs Interface Control Document on the NanoRacks website: NanoRacks.com
NanoLabs Interface Control Document

## Slide 15
Questions?
Mariel Rico
Payload Integration Engineer
mrico@nanoracks.com